## Slide 1: Software Tools GE84 Compatibility Analyses & GE84 Optimization
Hakim Ebdelli Broadcasting Services Division ITU/BR

## Slide 2
Content
  Exercise GE84 Compatibility Analyses
  Exercise GE84 Optimization

## Slide 3
Access to eTools
https://www.itu.int/ITU-R/eTerrestrial/eBroadcasting/ECalculations

## Slide 4
GE84 Compatibility Analyses
  The GE84 compatibility analysis tool features can be performed in the following contexts:
  When coordinating with affected administrations, you may want to perform a more precise examination in order to identify the potentially affected stations and the administrations with which you need to seek agreement.
  To perform a detailed analysis on frequency assignments published in Part A of the GE84 Special Section in order to assess their impact on your own frequency assignments.
  To analyse, in your planning process, available frequencies for new sound broadcasting services created using GE84_Optimization tool.
  Goal:
  Assess the impact to and from other emissions of a new or existing FM service, in accordance with Article 4 procedure of the Agreement.
  The values are calculated by the method contained in Annex 2, Chapter 4, at the transmitter site of the stations which are likely to be affected.

## Slide 5
GE84 Compatibility Analyses – Exercise
Prepare a new requirement (notice) to the GE84 plan, assigned to a sound broadcasting station located in TASHKENT city at 96.7 MHz, in vertical polarization
Evaluate, for this proposed modification:
The usable field strength (Eu) of the proposed modification.
Current and proposed Eu of potentially affected assignments recorded in the plan.
Find solutions for resolving interference, if any.
Eu: Minimum value of the field strength necessary to permit a desired reception
Parameter | Value
Administration/Country | UZB
Notice Type | T01
Intent | ADD
Fragment | GE84
Adm Ref Id | GE84-T01-UZB
Site name | TASHKENT
Frequency[MHz] | 96.7
Longitude[DDDMMSS] | +0691400
Latitude[DDMMSS] | +411800
ERP[dBW] | 34
Polarization | V
Antenna directivity | ND
Antenna height AGL[m] | 160
Bandwidth[KHz] | 300
Transmission system | 4

## Slide 6
GE84 Compatibility Analyses – Exercise – Input Data
  Preparation of the Electronic Notice File (one file per job). The file can be created using:
  TerRaNotices tool available on the BRIFIC DVD or,
  myAdmin or eQuery tools on eBroadcasting platform.
  Remark: This preparation of the Electronic Notice File of Input data is valid for both the GE84 Compatibility Analysis and Optimization tools.
  The tools are automatically validating the notice file before its submission to the calculations.
  For any other purpose, a validation tool is available in TerRaNotices or online by eValidation at:
  https://www.itu.int/ITU-R/eTerrestrial/eValidation

## Slide 7
GE84 Compatibility Analyses – Exercise – Input Data
Creation & Validation
  TerRaNotices:
  1. Create the electronic notice file from scratch
  or
  2. Extract it from the BR IFIC
  3. Validate the file using online eValidation
  4. Save the file on your laptop.
  (To add notices to the same file, use the "drag& drop" capability in TerRaNotices)

## Slide 8
GE84 Compatibility Analyses – Exercise – Input Data
Creation & Validation
  eQuery:
  Define the selection criteria (only one Administration),
  Click on the button "Apply Filter" to get the summary list and select the notice to be analysed.
  Click on the button Generate e-notices (Export to SGML).

## Slide 9
GE84 Compatibility Analyses – Exercise – Input Data
Creation & Validation
myAdmin (Portal for Focal points only):
Select the fragment GE84
Click on the number of notices corresponding to the group of notices of interest
When the summary list appears, it is possible to refine the selection by ticking on "Use Filter"
Select the notice to be analysed
Click on the button Generate e-notices (export to SGML).

## Slide 10
GE84 Compatibility Analyses – Exercise – Input Data
Creation & Validation
NoticeGeneration

## Slide 11
GE84 Compatibility Analyses – Exercise
Launch the tool
Login to : https://www.itu.int/ITU-R/eTerrestrial/eBroadcasting/ECalculations
Choose the options GE84 and GE84 Compatibility Analyses
Click on the button New Calculation
Remark: the GE84 Compatibility Analysis detailed documentation is available under eTools Documentation
Important: Verify the options under “Configuration information”

## Slide 12
GE84 Compatibility Analyses – Exercise
Upload the Notice File and Submit it
Remark:
You will be informed when the results are ready by email
You can also follow the execution of your job in the calculation history

## Slide 13
GE84 Compatibility Analyses – Exercise
Results
Minimum value of the field strength necessary to permit a desired reception.
Eu calculated by the simplified multiplication method, considering the interfering stations listed in the "interferers" section

## Slide 14
GE84 Optimization
Used mainly to search for new frequencies
Has been developed to achieve efficient use of the 87.5- 108 MHz band for analogue sound broadcasting (FM) and to allocate new frequencies for FM broadcasting to meet the growing need for additional frequencies in all administrations that are part of the GE84 Agreement.
Allows to assess the impact of an FM requirement to and from other emissions, in accordance with Article 4 Procedure of the GE84 Agreement.
It allows the user to submit requirements with flexible frequencies (FLEX) as well as requirements with fixed frequencies to the calculations.
FLEX (Flexible frequency requirement):
      The entire FM band (from 87.6 to 107.9 MHz) is analysed in steps of 100 kHz.
      The goal is, as first step, to submit FLEX requirements in view to identify the most suitable frequencies.
      In the next steps, the user can start fixing frequencies until all FLEX requirements are assigned with a suitable fixed frequency.

## Slide 15
GE84 Optimization
How to use the Optimization tool

## Slide 16
GE84 Optimization – Exercise
Prepare a requirement (notice) on FLEX channel assigned to a sound broadcasting station based on the information from the previously generated notice TASHKENT-96.7, using
TerRaNotices tool and selecting the Administration of UZB as notifying administration.
Important:
Assigned frequency: should be 87.7
Station identification: should be FLEX

## Slide 17
GE84 Optimization – Exercise
Login to: https://www.itu.int/ITU-R/eTerrestrial/eBroadcasting/ECalculations (TIES account needed)
Select the GE84 Optimization option.
Push the button New Calculation
Add/Drop the electronic notice file(s) previously prepared.
Upload the electronic notice file(s)
Finally Submit the uploaded notice file(s) (Submit button).
Important: check the options in the configuration information.
Note: You will be notified at your TIES email account when the job is complete. You can also monitor the status of your submission int the calculation history.

## Slide 18
GE84 Optimization – Exercise
New calculation, upload and submit
1
4
3
2

## Slide 19
GE84 Optimization – Exercise
Results
Requirement
Green means Assignable channel

## Slide 20
Thank you!
ITU – Radiocommunication Bureau
Questions to:
brbcd@itu.int
brmail@itu.int