## Slide 1: GE84 Agreement Procedures
Hakim Ebdelli Broadcasting Services Division ITU/BR

## Slide 2
Content
  GE84 Agreement Overview
  Procedure under Article 4
  Introduction of Digital Modulation
  The Reference Situation
  Notification to the Master Register (Article 7)

## Slide 3
Relating to the Use of the Band 87.5 - 108 MHz for FM Sound Broadcasting (Region 1 and Part of Region 3)
  204 channels
  100kHz channel spacing
The Geneva 84 Agreement

## Slide 4
  Article 13:
    Entry into force on 1 July 1987, at 0001 hours UTC.
    Established for a period of 20 years.
    Shall remain in force until it is revised by a competent administrative radio conference.
  Number of assignments:
  1987 : 51 168 recorded frequency assignments
  Now : > 96 000 recorded assignments > 13 000 pending modifications in coordination
The Geneva 84 Agreement
Assignments / Transmission Sytem
Assignments / Bandwidth (System 4)

## Slide 5
Procedure under Article 4
The agreement provides for a Plan modification procedure, described in Article 4.
The procedure allows for modifying the characteristics of a frequency assignment or entering a new assignment.
The procedure outlined in Article 4 takes into consideration not only sound broadcasting stations but also other services (BT, ILS/VOR, fixed, mobile).

## Slide 6
Article 4 – Services likely to be affected (Coordination required)
Other VHF-FM sound broadcasting stations (4.2.2 a)
ST61 television assignments in the band 87.5 – 100 MHz (4.2.2 b)
Fixed and mobile services (4.2.2 c, d)
Aeronautical Radionavigation Service above 108 MHz (4.2.2 f)

## Slide 7
Article 4 – Services likely to be affected (Coordination required)

## Slide 8
Article 4 – Services likely to be affected (Coordination required)
Other VHF-FM sound broadcasting stations
ST61 television assignments in the band 87.5 – 100 MHz
Fixed and
Mobile services
Aeronautical radionavigation services

## Slide 9
Border
Nearest point to the Border
Distance from BC station
BC Station
Country B
Country A
Article 4 – Coordination with other Sound/TV broadcasting services VHF-FM
Distance between the broadcasting station and the nearest point on the boundary of any other administration shall be used to identify administrations whose sound broadcasting services may be considered as affected

## Slide 10
Annex 4 of the Agreement:
    Tables 4.1- 4.4 : limits for protection of BC (Sound)
    Tables 4.5 to 4.7: limits for protection of BT (TV)
Coordination distances depend on:
  ERP
  Effective antenna height
  Propagation path (land, warm/cold seas and areas of super refractivity)
Article 4 – Coordination with other Sound/TV broadcasting services VHF-FM

## Slide 11
Article 4 – Agreement to proposed BC station
Coordination between administrations on the basis of a table of distances (Annex 4)
Plan modification should normally be accepted by affected administration on the basis of the following technical criteria for the protected station:
  Resulting Eu <= 54 dB(µV/m) (sound)
  Resulting Eu <= 52 dB(µV/m) (television)
  Resulting Eu increase <= 0.5 dB relative to reference Eu (Eu-ref) if limit a) or b) is exceeded.

## Slide 12
Article 4 – Coordination with fixed & mobile services
BC Station
Border
Nearest point to the Border
FS from BC station
Country A
Country B
Fixed service : 0 dB (mV/m)
Land mobile service: limits depend on the POL of the BC station:
  Region 3 (87.5-100 MHz)
    H pol: 18 dB(mV/m)
    V/M pol: 0 dB(mV/m)
Fixed & mobile services are considered as to be affected if field strength (FS) of BC at the nearest point on the boundary of another administration exceeds established limits

## Slide 13
500 km
Article 4 – Coordination with ARNS
Aeronautical RadioNavigation Service (ARNS) in the band 108 - 117.975 MHz
Distance to the nearest point on the border < 500 km
(Chapter 3 of Annex 4)

## Slide 14
No agreement required if modifications involve:
  Less interference – lower ERP
  Distance to border > coordination limits
  Small change in site location
    15 km ERP >= 1kW
    5 km < 1kW
    Provided that the change in topographical conditions does not increase the probability of interference caused to the stations of other countries.
Article 4 – Quick Modification Procedure (§4.2.4)

## Slide 15
Notification
ADD
MOD
SUPPRESS
Completeness & Receivability Check
Return to Adm
Plan & Coordination Examination
Publication in Part A
of the Special Section
(ACK + COORD)
100 days Coordination & Comments Period Expired?
SUPPRESS?
Publication in Part C
of the Special Section
(ACK)
Deletion from the Plan
&
Reference Situation
Complete Coordination
Checking Examination
Request from NOTIFIER for Part B Publication?
Are there any OBJECTIONS?
Publication in Part B
Of the Special Section
Recording in the Plan
&
Reference Situation
Contact and inform the Notifying Adm
NO
NO
NO
OK
NO
YES
YES
NO
YES
YES
Article 4 – Plan modification Procedure

## Slide 16
Article 4 – Plan modification Procedure
Notification:
  T01 notice form for Addition or Modification to the Plan
  TB5 notice for Suppression or Withdrawal
Coordination:
  No comment = AGREEMENT
Publication in Part B
  Must be requested for publication in Part B (TB3 notice)
  Publication in Part B only if no objections
Important
  Pursuant to paragraphs 1.3 of Part A2 and 4.6.1 of Part A5 of the Rules of Procedure (RoP) the frequencies pending in coordination stage are deleted after 2 years and 100 days

## Slide 17
Article 4 – Publications
Proposed modifications are published in a Special Section annexed to BR IFIC.
Part A :
  Details of proposed new assignments and/or changes of already recorded assignments
  Information submitted by notifying administration (COORD COMPLETED, Source NOTIFIER)
  Coordination information as a result of BR examination (COORD REQUIRED, Source ITU)
Part B:
  Details of proposed new assignments and/or changes in characteristics of already recorded assignments on which all agreements have been reached;
  Assignments are being published in Part B after 100-day period if NO OBJECTIONS have been received and if notifying administration has sent a relevant request to the BR (TB3).
Part C: Details of assignments to be suppressed from the Plan.

## Slide 18
Introduction of Digital Modulation
  Provision 3.1 of Chapter 3 of Annex 2 provides, in addition to the 5 transmission systems defined as variants, the introduction of Digital Modulation on the conditions that this:
    Does not cause higher interference, and
    Does not require greater protection than the reference system mentioned in the Plan.

## Slide 19
The Reference Situation
Extract of the GE84 Agreement :
  “The reference Eu of an assignment to be protected is the FS which results from the Plan at the time this assignment was first recorded in the Plan. The reference situation is re-evaluated after each GE84 Special Section for the notices published in Part B when they are recorded into the Plan.”
    If, following the introduction of new contributors in the Plan, the usable field strength of an assignment recorded in the Plan becomes higher than the Eu-ref, the Eu-ref calculated at the time an assignment is recorded in the Plan remains unchanged.
    But, “if, due to deletions or modifications, the usable field strength becomes lower, then this lower value becomes the new Eu-ref .”

## Slide 20
The Reference Situation
The Eu calculations are performed at the transmitter site of the affected station.
They are considering the 20 highest contributors RECORDED in the Plan.
They are not considering the notices in process in the Plan and not yet RECORDED (TIP notices)
No polarization discrimination is applied.

## Slide 21
The Reference Situation
The details of the Eu and Eu Ref calculations (details of the top 20 contributors) are published in the BR IFIC. The updated reference situation is visible in the BR IFIC following a Part B publication.
Details of the contributors

## Slide 22
Notification to the Master Register (Article 7)
When an administration proposes to bring into use an assignment, it shall notify its characteristics to the BR in accordance with the provisions of Article 11 of the Radio Regulations.
When the assignment brought into use conforms to the technical characteristics described for this assignment in the Plan, it is then recorded in the Master International Frequency Register (commonly called the MIFR).

## Slide 23
Assistance from BR (4.3.13)
Administration may request BR assistance in:
  Seeking agreement from another ADM
  Applying of the Article 4 procedure at any stage
  Carrying out technical studies in relation to this procedure
  GE84 compatibility analysis and GE84 Optimization are available on eTools at :
  https://www.itu.int/ITU-R/eTerrestrial/eBroadcasting/ECalculations

## Slide 24
Thank you!
ITU – Radiocommunication Bureau
Questions to brmail@itu.int or brbcd@itu.int